| Model | MP500 |
| --- | --- |
| Swing over bed | 420mm |
| Swing over cross slide | 180mm |
| Distance between centers | 500mm |
| Taper of spindle bore | MT3# |
| Spindle bore | 28mm |
| Spindle speed | 160—1360rpm |
| Metric threading | 0.2—6mm |
| Inch threading | 120—4TPI |
| Worktable size | 160x475mm |
| Travel of cross slide | 200mm |
| Travel of compound slide | 80mm |
| Tailstock quill travel | 70mm |
| Taper of tailstock quill | MT3# |
| Motor for lathe | 550W |
| Drilling capacity | 15mm |
| End milling capacity | 20mm |
| Face milling capacity | 63mm |
| Spindle speed | 117—1300rpm |
| Spindle taper | MT 3# |
| Spindle travel | 85mm |
| Spindle nose to table | 310mm |
| Mill-drill head swivels | 360º |
| Motor for drill/mill | 550W |
| Net weight | 230kg |
| Packing Size | 1120x580x1150 |

| Self-centering three jaw | 1 set |
| --- | --- |
| Dead centers MT4 and MT2 | 1 set |
| Metal change gear | 1 set |
| Full size splash guard | 1 set |
| Drilling chuck with taper shanl | 1 sets |
| Drawbar | 1 set |
| Necessary tools and tool kit | Numbers |