| Document No. | QSP0701-101LG-01 |
| --- | --- |
| Edition | B/0 |
| Model | LM-101LG |
| Date | 2013-01-10 |
| Page | 3 |

Fire Detecting Wireless Online Alarm Instruction

Customer setup

Fiction：

Audit：

Approve：

LM-101LG Customer usage and installation

一、Appearance and dimension（Figure 1）

Figure 1

二、use

1、Function diagram of cover, base and mounting plate（Figure 2）

Figure 2

2、Battery mount（Figure 3）

A、Take out the product from packing box, rotate mounting plate anticlockwise, take out the 9 V and 1.5 V battery,remove the protective film on the battery respectively.

B、Put 9 v battery into the battery compartment and pay attention to The battery polarity symbol in compartment；

C、Please turn bayonet lock rocker to inwall before put 1.5V battery into compartment and pay attention to The battery polarity symbol in compartment；

D、Aim  raised two hooks on mounting plate to two card slot on base .rotate mounting plate clockwise till hooks enter into card slot totally.

Figure 3

三、Installation sketch map（Figure 4）

1、Choose a suitable installation position and effective communication distance;

2、According to the holes of the installation board, drill a hole in the needed place of ceiling and stuff the plastic nail seat into the hole;

3、Use the screw to fix the installation panel onto plastic nail seat;

4、Embed the two detector base hook into the detector slot. Turn the smoke detector clockwise in order to fasten it to the installation panel tightly.

5、After installation, carry out the actual communication test to prevent the communication fault.

Figure 4

四、Technical parameters

1、Executive standard：			BS EN 14604-2005

2、Working voltage：			    DC9V（for smoke detector）

DC4.5V（for wireless online：1.5VX3节）

3、Working current：：			DC9V quiescent current≤10uA

DC9V alarm current≤ 20mA

DC4.5V quiescent current≤230uA

DC4.5V working current≤4mA

4、Alarm decibel：			    ≥85dB/3m

5、Alarm indicator：			    red LED

6、Online/learn indicator：  	red/green LED

7、Frequency：			        433.92MHz

8、Transmission distance：		spacious straight-line distance≤60m

9、Working temperature：			-10℃~+40℃

10、Ambient humidity：			≤95%RH（no condensation）

11、Low battery test：		    DC9V（for smoke detector）＜7.35V

A brief alarm sound in about every 43 seconds

DC4.5V（for wireless online）＜3.3V

A brief alarm sound in about every 60 seconds

五、Recommended Replacement Batteries

Pair Deer 9V 6F22

GP       9V 1604S

Mustang  9V 6F22

Pair Deer  9V 6LR61

GP       9V 1604A

Pair Deer  3 x 1.5V	LR6/AA

GP        3 x 1.5V GP15AU

Mustang   3 x 1.5V LR6/AA

# Text boxes

1.5V battery card slot下、

9V battery card slot、

9V battery

card slot

1.5V battery

online/learn indicator (red/green LED)

learn button

Test  button

Alarm indicator

（red LED）

base

cover

buzzer

screw hole

hook

mounting plate