| Model | VMC850P |
| --- | --- |
| Worktable |  |
| Size of working table | 500x1000mm |
| T slots | 5x18x100 |
| Capacity |  |
| Max. spindle speed | 8000rpm |
| Spindle taper / Tool holder | BT40 |
| Power of spindle motor | 11kw/15kw |
| Max. loading of working table | 500kg |
| Travel |  |
| X axis travel | 850mm |
| Y axis travel | 500mm |
| Z axis travel | 550mm |
| Feed (direct drive) |  |
| Feeding speed | 12000mm/min |
| X axis rapid feeding speed | 48m/min. |
| Y axis rapid feeding speed | 48m/min. |
| Z axis rapid feeding speed | 32m/min. |
| Machining range |  |
| Spindle nose to table | 100-650mm |
| Spindle center to column | 582mm |
| Tool magazine |  |
| Tool magazine capacity | 24 |
| Max. length of tool | 300mm |
| Tools change time | 2.5s |
| Accuracy |  |
| Positioning accuracy (X/Y/Z) | ±0.008mm |
| Repeatability accuracy (X/Y/Z) | ±0.004mm |
| Other's |  |
| Net weight | 5500kg |
| Machine dimension | 2460x2355x2860mm |

| Controller | 1 set |
| --- | --- |
| Auto lubrication system | 1 set |
| Coolant system | 1 set |
| Working lamp | 1 sets |
| Closed metal housing | 1 set |
| Necessary tools and tool kit | Numbers |