| Model | HL800 |
| --- | --- |
| Swing over bed | 800mm |
| Swing over carriage | 545mm |
| Swing over gap | 1000mm |
| Distance between centers | 1000/1500/2000/3000/4000mm |
| Bed width | 400mm |
| Spindle bore | 103mm |
| Steps & range of spindle speed | 18/9-1300rpm |
| Spindle taper | Metric 115 |
| Tool-post travel | 110mm |
| Cross travel | 325mm |
| Sleeve of tailstock travel | 130mm |
| Range of longitudinal feeds | 72/0.072-4.066mm/r |
| Range of transversal feeds | 72/0.036-2.033mm/r |
| Metric threads | 72/0.5-112mm |
| Inch threads | 72/56-0.25TPI |
| Module threads | 36/0.5-7MP |
| Pitch threads | 36/4-56DP |
| Tailstock taper | MT6 |
| Quill bore of tailstock | 90mm |
| Main motor power | 11kw |
| Rapid motor power | 250w |
| Net weight | 2900/3050/3400/3800/4200kg |
| Packing size | 2.85/3.35/3.85/4.85/5.85*1.12*1.85m |

| Self-centering 3 jaw chuck | 三爪自定心卡盘 | 1 set |
| --- | --- | --- |
| Independent 4 jaw chuck | 四爪单动卡盘 | 1 set |
| Dead center MT8 & MT5 | 莫氏#8；莫氏#5顶尖 | 1 set each |
| Metal change gear | 交换挂轮 | 1 set |
| Full size splash guard | 挡屑板 | 1 set |
| Follow rest & steady rest | 跟刀架，中心架 | 1 set each |
| Coolant pump | 冷却泵 | 1 set |
| Working Lamp | 照明灯 | 1 set |
| Face plate | 花盘 | 1 set |
| Stand with foot-brake | 柜式底座，脚刹 | 1 set |