| Model | HL660 |
| --- | --- |
| Swing over bed | 660mm |
| Swing over carriage | 420mm |
| Swing over gap | 790mm |
| Distance between centers | 1000/1500/2000/3000mm |
| Bed width | 330mm |
| Spindle bore | 80mm |
| Steps & range of spindle speed | 15/24-1600rpm |
| Spindle taper | MT8 |
| Tool-post travel | 130mm |
| Cross travel | 300mm |
| Sleeve of tailstock travel | 130mm |
| Range of longitudinal feeds | 66/0.072—4.038mm/r |
| Range of transversal feeds | 66/0.036—2.019mm/r |
| Metric threads | 66 / 0.5—28mm |
| Inch threads | 66 / 1—56TPI |
| Module threads | 33 / 0.5—3.5MP |
| Pitch threads | 33 / 8—56DP |
| Tailstock taper | MT5 |
| Quill bore of tailstock | 130mm |
| Main motor power | 7.5kw |
| Rapid motor power | 250w |
| Net weight | 1650/1800/1950/2450kg |
| Packing size | 2.42/2.92/3.42/4.42x1.12x1.80m |

| Self-centering 3 jaw chuck | 三爪自定心卡盘 | 1 set |
| --- | --- | --- |
| Independent 4 jaw chuck | 四爪单动卡盘 | 1 set |
| Dead center MT8 & MT5 | 莫氏#8；莫氏#5顶尖 | 1 set each |
| Metal change gear | 交换挂轮 | 1 set |
| Full size splash guard | 挡屑板 | 1 set |
| Follow rest & steady rest | 跟刀架，中心架 | 1 set each |
| Coolant pump | 冷却泵 | 1 set |
| Working Lamp | 照明灯 | 1 set |
| Face plate | 花盘 | 1 set |
| Stand with foot-brake | 柜式底座，脚刹 | 1 set |