| Model | BL330C/BL330C-1 |
| --- | --- |
| Swing over bed | 330mm |
| Swing over carriage | 160mm |
| Distance between centers | 600 / 750mm |
| Bed width | 160mm |
| Spindle bore | 38mm |
| Spindle taper | MT5 |
| Steps of spindle speed | 12 |
| Spindle speed | 60-1650rpm |
| Tool post travel | 100mm |
| Cross travel | 160mm |
| Range of longitudinal feeds | 0.1 - 1.5mm/r |
| Range of cross feeds | 0.045 - 0.6mm/r |
| Metric threads | 20 / 0.5-9mm |
| Inch threads | 28 / 56-4tpi |
| Max. travel of tailstock sleeve | 85mm |
| Taper of tailstock sleeve | MT3 |
| Motor power | 1100W |
| Net weight | 320kg |
| Packing size | 1320 /1570x760x700mm |

| Items Description | Quantity |
| --- | --- |
| Dia. 160mm self-centering 3 jaw chuck | Ø160三爪自定心卡盘 | 1 set |
| Dead center MT4 & MT2 | 莫氏#3；莫氏#2顶尖 | 1 set each |
| Metal change gear | 交换挂轮 | 11 sets |
| Allen wrenches (4,5,6,8) | 六角扳手 | 1 set each |
| Bolt & washer | 螺栓及垫片 | 4 sets each |
| Full size splash guard | 挡屑板 | 1 sets |